## Slide 1: Microprocessors, Microcontrollers & Embedded systems
8051 architecture

## Slide 2: 8051 Programming model
Internal ROM address: 0x000-0xFFF
Internal RAM address: 0x00-0x7F
  Four register banks: 0x00-0x1F
  Bit addressed RAM: 0x20-0x2F
  General purpose RAM: 0x30-0x7F
Special function Registers
  Specific addresses between 0x80-0xF0
External memory access:
  If EA = 0, external address: 0x1000-0xFFFF
  If EA = 1, external address: 0x0000-0xFFFF
8051 programming model
7F
Notes: EA = 0 implies EA bar = 1

## Slide 3: 8051 Special function registers
Accumulator
B Register
PC
PSW
SP
Data pointer
Ports 0 to 3: P0, P1, P2, P3
Serial data buffer SBUF
Timer Registers: (TH0, TL0) & (TH1, TL1)
Control registers: IP, IE, TMOD, TCON, SCON & PCON: Contain the control and status bits for interrupts, timers/counters & serial port
Each of these registers have an 8-bit address except the PC
Why is the address necessary?
Refer to 8051 datasheet: Page 8
https://www.nxp.com/docs/en/data-sheet/8XC51_8XC52.pdf
Notes: Typically, arithmetic and logical operations take place during Phase 1 and internal register-to-register transfers take place during Phase 2.

## Slide 4: 8051 Special function registers
Present in new variants of 8051
Present in new variants of 8051

## Slide 5: 8051 Special function registers
Notes: Typically, arithmetic and logical operations take place during Phase 1 and internal register-to-register transfers take place during Phase 2.

## Slide 6: 8051 External memory interface
External memory interface up to 64kbytes of Program and/or data memory possible
External Program memory access
Fetch always uses 16-bit address
Access uses as the read strobe
Memory location obtained from P0 & P2 (always 16-bit address)
ALE multiplexes data and lower 8 bits of address
Access to external memory either with active or with PC having address larger than internal memory
External Data memory access
Fetch can be 8-bit or 16-bit address
Access uses and as read and write strobes
Memory location obtained from both P0 & P2 (for 16-bit addr) or P0 alone (for 8-bit addr)
ALE multiplexes data and lower 8 bits of address
Access to external memory with and active
Notes: Typically, arithmetic and logical operations take place during Phase 1 and internal register-to-register transfers take place during Phase 2.

## Slide 7: 8051 External Program memory interface
External Program memory with internal ROM
External Program memory without internal ROM
8-bit latch such as 74LS373 to demultiplex data and address lines
8051 microcontroller
Internal ROM 4K
(0x0000-0x0FFF)
External
Program
memory
(60K)
Latch
D0-D7
A8-A15
P2
P0
A0-A7
8051 microcontroller
Internal ROM 4K
(0x0000-0x0FFF)
External
Program
memory
(64K)
Latch
D0-D7
A8-A15
P2
P0
A0-A7

## Slide 8: 8051 External Program memory interface
External Program memory execution
From 8051 Hardware manual
(A)
(B)
When is (A) used & when is (B) used?
Notes: When internal data memory is being used (i.e., without using MOVX instructions), the execution in (A) is adopted.
When external data memory is used (i.e., with MOVX instructions), the execution in (B) is adopted

## Slide 9: 8051 External Data memory interface
External Data memory with internal ROM
External Program & Data memory
8051 microcontroller
Internal ROM 4K
(0x0000-0x0FFF)
External
Data
memory
(64K)
Latch
D0-D7
A8-A15
P2
P0
A0-A7
Is anything missing?
Is something wrong?
8051 microcontroller
External
Program
memory
(64K)
Latch
D0-D7
A8-A15
P2
P0
A0-A7
External
Data
memory
(64K)
A8-A15
D0-D7
A0-A7
Notes: ALE is missing

## Slide 10: Interfacing additional peripherals with 8051
IO-mapped IO
Computer/controller uses two separate address spaces for memory & IO devices
Available addresses for memory is unaffected by IO
Instructions used for IO & memory operations are different
Limited number of IO that can be interfaced
Efficient
Memory-mapped IO
Computer/controller uses the same address space for memory & IO devices
Available addresses for memory is reduced due to IO
Instructions used for IO & memory operations are same
Significantly large number of IOs can be interfaced
Less efficient
Why is Memory-mapped IO less efficient?
Notes: Memory-mapped I/O has to send address of the I/O in the first two memory cycles and then data can be parsed to I/O. In IO-mapped IO, data can be parsed directly with the control signal concurrently parsed.

## Slide 11: 8051 with 8255
Intel 8255
Programmable peripheral interface
I/O mapped I/O
8051 microcontroller
8255
D0-D7
P0
PA0-PA7
PB0-PB7
PC0-PC7
Memory mapped I/O
8051 microcontroller
8255
74LS245
D0-D7
P0
PA0-PA7
PB0-PB7
PC0-PC7
Latch
Decoder
P2